## Slide 1: TURBINE AND PUMP
 A turbine is a rotary engine that extracts energy from a fluid flow and converts it into useful work
Eg: steam turbine, gas turbine, hydraulic turbine
 Hydraulic Turbines transfer the kinetic energy and potential energy of water into a rotation .
 We can generate electricity by coupling to electric generator
 Pump is work consuming device and it is just opposite to turbine.
Eg. Centrifugal pump

## Slide 2: CLASSIFICATION OF HYDRAULIC TURBINES:
BASED ON FLOW PATH
  Axial Flow
  Radial Flow
  Tangential Flow
  Mixed Flow
Based on flow path
 Axial Flow Hydraulic Turbines: flow path of the liquid mainly parallel to the axis of rotation. Eg: Kaplan turbine
 Radial Flow Hydraulic Turbines: liquid flowing mainly in a plane perpendicular to the axis of rotation.
 Tangential Flow Hydraulic Turbines: liquid flowing mainly in a plane tangential to the turbine. Eg: Pelton turbine

## Slide 3
Mixed Flow Hydraulic Turbines: For most of the Hydraulic Turbines used there is a significant component of both axial and radial flows. They are called as Mixed Flow Turbines.
eg.Francis Turbine is an example of mixed flow type, in Francis Turbine water enters in radial direction and exits in axial direction.
3. BASED ON WORKING PRINCIPLE
 Impulse turbine
 Reaction turbine
Stator
runner
Kinetic energy changes but pressure energy remains constant
Kinetic energy changes and pressure energy
Fig Impulse machine

## Slide 4
Pressure change occur only in the nozzles of the machine. Eg : Pelton Turbine.
The change in fluid velocity and reduction in its pressure causes a reaction on the turbine
blades.
Eg: Francis and Kaplan Turbines
Stator
runner
Kinetic energy changes as wellas pressure energy also changes
Kinetic energy changes and pressure energy
Fig Reaction machine

## Slide 5
SL NO | IMPULSE TURBINE | REACTION TURBINE
1 | Impulsive force is rotating the turbine | Reaction force is rotating turbine
2 | Pressure of liquid is decreasing in nozzle before entering to turbine | Pressure decreases as it flows over the blades
3 | Blades are of symmetrical profile | Blades having aerofoil profile
4 | The size of turbine is small for the same power output | Size of reaction turbine is large for the same power output
5 | Whole pressure energy of water is converted into kinetic energy before passed onto turbine wheel | Part of pressure energy only converted to kinetic energy
6 | Water discharges directly from turbine wheel to tail race | Water discharges into a draft tube then it is finally discharged to tail race
7 | Pressure of water will be atmospheric as it flows over moving blades | Pressure of water continuously decreases as it flows over the blades

## Slide 6: PELTON TURBINE POWER PLANT

## Slide 7: PELTON TURBINE

## Slide 8: REACTION TURBINE

## Slide 9: Francis Turbine

## Slide 10: Kaplan Turbine:

## Slide 11: CLASSIFICATION OF PUMPS
Pumps are broadly classified into
Positive- displacement pumps
Rotodynamic pumps
 Positive- displacement pumps: They make a fluid move by trapping a fixed amount and displacing the trapped volume into the discharge pipe. Discharge is directly proportional to speed.
Eg : Reciprocating pump, Vane pump, Gear pump
 Rotodynamic pumps: It is a machine in which energy is continuously imparted to the pumped fluid by means of a rotor and thus fluid is raised to higher elevation.
Eg: Centrifugal pump

## Slide 12: RECIPROCATING PUMP

## Slide 13: Centrifugal pumps

## Slide 15: Rotary vane pump

## Slide 16: Scroll Pump
Intake
Exhaust port in center
Blue area rotates counterclockwise
with silver area sprung against it. Volume between parts decreases.

## Slide 17: Pressure
 Fluid pressure = Normal compressive force
Area
 It is compressive in nature
 S.I unit is Pascal
 1 atm pressure=101325 pa
 1 atm pressure=1.o1325 bar
 1 atm pressure=101.325 Kpa
 1 atm pressure=10.3 mtr of water
 1 atm pressure=76cm of Hg
 Atm pressure is measured by barometer
 It is scalor quantity Acq. To pascal law

## Slide 18: Pressure of fluid expressed in 3 forms
 Absolute pressure
 Gauge pressure
 Negative gauge
P>Patm
Patm
P<Patm
P=0
Gauge pressure
Vacuum pressure
Absalute pressure
Absalut e pressur e

## Slide 19: Pascal law:

## Slide 20: Pressure Variation in a Fluid at Rest- Hydrostatic law

## Slide 21: Pressure measuring instruments:
Simple manometers
 Peizometer
 U-tube manometer
 Single column manometer
Differential manometer
 2piezometer d.f
 Inverted u-tube manometer
 U-tube differential manometer
Pressure gauges
 Bourdon tube pressure gauges
 Diaphragam pressure gauges

## Slide 22: Manometers
Principle of operation: Manometers are devices in which columns of suitable liquid are used to measure the difference in pressure between two points, or between a certain point and the atmosphere (patm).
Applying fundamental equations of hydrostatics the pressure difference, P, between the two liquid columns can be calculated.

## Slide 23: PEIZOMETER

## Slide 24: U-TUBE MANOMETER

## Slide 25: Single column manometer

## Slide 27: U-tube differential manometer

## Slide 29: Micromanometer

## Slide 30: Bourdon Gauge (Mechanical)

## Slide 31: Diaphragm pressure gauge

## Slide 33: Thank You